## Slide 1
Multiple Access Protocols
Lecture12-14 (Theory)

## Slide 2
Index
,
Concept Multiple Access Resolution
Random Access Control
  ALOHA(Pure and Slotted ALOHA)
  Carrier Sense Multiple Access
  Carrier Sense Multiple Access with Collision Detection
  Carrier Sense Multiple Access with Collision Avoidance

## Slide 4
Multiple-access protocols

## Slide 5
Random Access
In Random access or Contention methods, no station is superior to another station and none is assigned the control over another. No station permits, or does not permit, another station to send. At each instance, a station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.

## Slide 6
Frames in a pure ALOHA network

## Slide 7
Figure 4 Procedure for pure ALOHA protocol
Procedure for pure ALOHA protocol

## Slide 8
The stations on a wireless ALOHA network are a maximum of 600 km apart. If we assume that signals propagate at 3 × 108 m/s, we find
Tp = (600 × 105 ) / (3 × 108 ) = 2 ms.
Now we can find the value of TB for different values of K .
a. For K = 1, the range is {0, 1}. The station needs to| generate a random number with a value of 0 or 1. This means that TB is either 0 ms (0 × 2) or 2 ms (1 × 2), based on the outcome of the random variable.
Example 1

## Slide 9
b. For K = 2, the range is {0, 1, 2, 3}. This means that TB can be 0, 2, 4, or 6 ms, based on the outcome of the random variable.
c. For K = 3, the range is {0, 1, 2, 3, 4, 5, 6, 7}. This means that TB can be 0, 2, 4, . . . , 14 ms, based on the outcome of the random variable.
d. We need to mention that if K > 10, it is normally set to 10.
Example 1 (continued)

## Slide 10
Figure 5 Vulnerable time for pure ALOHA protocol
Vulnerable time - pure ALOHA protocol

## Slide 11
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the requirement to make this frame collision-free?
Example 2
Solution
Average frame transmission time Tfr is 200 bits/200 kbps or 1 ms. The vulnerable time is 2 × 1 ms = 2 ms. This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the one 1-ms period that this station is sending.

## Slide 12
The throughput for pure ALOHA is S = G × e −2G .
The maximum throughput
Smax = 0.184 when G= (1/2).

## Slide 13
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
Example 3
Solution
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. The load is 1. In this case S = G× e−2 G or S = 0.135 (13.5 percent). This means that the throughput is 1000 × 0.135 = 135 frames. Only 135 frames out of 1000 will probably survive.

## Slide 14
Example 3 (continued)
b. If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e −2G or S = 0.184 (18.4 percent). This means that the throughput is 500 × 0.184 = 92 and that only 92 frames out of 500 will probably survive. Note that this is the maximum throughput case, percentagewise.
c. If the system creates 250 frames per second, this is (1/4) frame per millisecond. The load is (1/4). In this case S = G × e −2G or S = 0.152 (15.2 percent). This means that the throughput is 250 × 0.152 = 38. Only 38 frames out of 250 will probably survive.

## Slide 15
Figure 6 Frames in a slotted ALOHA network
Frames in a slotted ALOHA network

## Slide 16
The throughput for slotted ALOHA is S = G × e−G .
The maximum throughput Smax = 0.368 when G = 1.

## Slide 17
Figure 7 Vulnerable time for slotted ALOHA protocol
Vulnerable time for slotted ALOHA protocol

## Slide 18
A slotted ALOHA network transmits 200-bit frames on a shared channel of 200 kbps. What is the throughput if the system (all stations together) produces
a. 1000 frames per second b. 500 frames per second
c. 250 frames per second.
Example 4
Solution
The frame transmission time is 200/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, this is 1 frame per millisecond. The load is 1. In this case S = G× e−G or S = 0.368 (36.8 percent). This means that the throughput is 1000 × 0.0368 = 368 frames. Only 386 frames out of 1000 will probably survive.

## Slide 19
Example 4 (continued)
b. If the system creates 500 frames per second, this is (1/2) frame per millisecond. The load is (1/2). In this case S = G × e−G or S = 0.303 (30.3 percent). This means that the throughput is 500 × 0.0303 = 151. Only 151 frames out of 500 will probably survive.
c. If the system creates 250 frames per second, this is (1/4) frame per millisecond. The load is (1/4). In this case S = G × e −G or S = 0.195 (19.5 percent). This means that the throughput is 250 × 0.195 = 49. Only 49 frames out of 250 will probably survive.

## Slide 20
Figure 8 Space/time model of the collision in CSMA
Space/time model of the collision in CSMA

## Slide 21
Vulnerable time in CSMA
Figure 9 Vulnerable time in CSMA

## Slide 22
Figure 10 Behavior of three persistence methods
Behavior of three persistence methods

## Slide 23
Figure 11 Flow diagram for three persistence methods
Flow diagram for three persistence methods

## Slide 24
Figure 12 Collision of the first bit in CSMA/CD
Collision of the first bit in CSMA/CD

## Slide 25
Figure 13 Collision and abortion in CSMA/CD
Collision and abortion in CSMA/CD

## Slide 26
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal, as we see later) is 25.6 μs, what is the minimum size of the frame?
Example 5
Solution
The frame transmission time is Tfr = 2 × Tp = 51.2 μs. This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision. The minimum size of the frame is 10 Mbps × 51.2 μs = 512 bits or 64 bytes. This is actually the minimum size of the frame for Standard Ethernet.

## Slide 27
Flow diagram for the CSMA/CD
Figure 14 Flow diagram for the CSMA/CD

## Slide 28
Flow diagram for the CSMA/CD
Figure 14 Flow diagram for the CSMA/CD

## Slide 29
Energy level during transmission, idleness, or collision
Figure 15 Energy level during transmission, idleness, or collision

## Slide 30
Timing in CSMA/CA
Figure 16 Timing in CSMA/CA

## Slide 31
In CSMA/CA, the IFS can also be used to define the priority of a station or a frame.

## Slide 32
In CSMA/CA, if the station finds the channel busy, it does not restart the timer of the contention window;
it stops the timer and restarts it when the channel becomes idle.

## Slide 33
Flow diagram for CSMA/CA
Figure 17 Flow diagram for CSMA/CA

## Slide 34: Practice Questions
https://pinoybix.org/2017/07/mcq-in-network-layer-internet-protocol-forouzan.html
https://edurev.in/course/quiz/attempt/-1_Test-Ipv4--IP-Packet/0decdb37-7206-4824-afdd-d47013a5c4cd