## Slide 1
Data Link Layer
Lecture10-11 (Theory)

## Slide 2
Index
,
Types of Errors
Redundancy
Error Detection
Error Correction

## Slide 3
TYPES OF ERRORS
Single bit error :-
  Only one bit in the data unit has changed.
Burst error :-
  It means that two or more bits in the data unit has changed.

## Slide 4
Single-bit error

## Slide 5
Basic concepts
Networks must be able to transfer data from one device to another with complete accuracy.
Data can be corrupted during transmission.
For reliable communication, errors must be detected and corrected.
Error detection and correction are implemented either at the data link layer or the transport layer of the OSI model.

## Slide 6
Single bit errors are the least likely type of errors in serial data transmission because the noise must have a very short duration which is very rare.
However this kind of errors can happen in parallel transmission.
Example:
If data is sent at 1Mbps then each bit lasts only 1/1,000,000 sec. or 1 μs.
For a single-bit error to occur, the noise must have a duration of only 1 μs, which is very rare.

## Slide 7
Burst error

## Slide 9
The term burst error means that two or more bits in the data unit have changed from 1 to 0 or from 0 to 1.
Burst errors does not necessarily mean that the errors occur in consecutive bits, the length of the burst is measured from the first corrupted bit to the last corrupted bit. Some bits in between may not have been corrupted.

## Slide 10
Data can be corrupted during transmission. For reliable communication, errors must be detected and corrected.
Error detection and correction are implemented either at data link layer or the transport layer of the OSI model.

## Slide 11
Burst error is most likely to happen in serial transmission since the duration of noise is normally longer than the duration of a bit.
The number of bits affected depends on the data rate and duration of noise.
Example:
If data is sent at rate = 1Kbps then a noise of 1/100 sec can affect 10 bits.(1/100*1000)
If same data is sent at rate = 1Mbps then a noise of 1/100 sec can affect 10,000 bits.(1/100*106)

## Slide 12: Error detection
Error detection means to decide whether the received data is correct or not without having a copy of the original message.
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.
Notes: Make sense of message.
Make sense of message.

## Slide 13: Redundancy
Instead of repeating the entire data stream, a shorter group of bits may be appended to the end of each unit.
This technique is called Redundancy because the extra bit are redundant to the information. They are discarded as soon as the accuracy of the transmission has been determined.

## Slide 14
There are basically four types of redundancy checks. They are:
  1. VRC (Vertical Redundancy Check).
  2. LRC (Longitudinal Redundancy Check).
  3. CRC (Cyclical Redundancy Check).
  4. Checksum

## Slide 15
Redundancy

## Slide 16
Four types of redundancy checks are used in data communications

## Slide 17
Vertical Redundancy Check
It is also known as parity check
It is least expensive mechanism for error detection
In this technique, the redundant bit called parity bit is appended to every data unit so that the total number of 1s in the unit becomes even (including parity bit)
17

## Slide 18
Vertical Redundancy Check
Checking function
Is total number of 1s even ?
Receiver
1100001 | 1
Even – parity generator
1
1100001 Data
18
Sender

## Slide 19
Vertical Redundancy Check VRC

## Slide 20

Example :
1110110 1101111 1110010
- After adding the parity bit 11101101 11011110 11100100
VERTICAL REDUNDANCY CHECK
20

## Slide 21
VRC can detect all single – bit errors
It can detect burst errors if the total number of errors in each data unit is odd.
VRC can not detect errors where the total number of bits changed is even.
Vertical Redundancy Check

## Slide 22
LONGITUDINAL REDUNDANCY CHECK(LRC)
In this method , a block of bits is organized in table(rows and columns)
calculate the parity bit for each column and the set of this parity bit is also sending with original data.
From the block of parity we can check the redundancy.

## Slide 23
Longitudinal Redundancy Check LRC

## Slide 24: LRC Example
11100111 1101101 00111001 10101001 10101010
11100111
11011101
00111001
10101001
11100111 11011101 00111001 10101001
LRC
10101010
Original data plus LRC

## Slide 25: Suppose the following block is sent :
LRC Example
10101001 00111001 11011101 11100111 10101010
(LRC)
However,it is hit by burst of length eight and some bits are corrupted (Yellow bits are changed) :
10100011 10001001 11011101 11100111 10101010
(LRC)
When the receiver checks the LRC,some of the bits are not following even parity rule and whole block is discarded (the non matching bits are shown in red )
10100011 10001001 11011101 11100111 10101010

## Slide 26
Advantage :
-> LRC of n bits can easily detect burst error of n bits.
Disadvantage :
-> If two bits in one data units are damaged and two bits in exactly same position in another data unit are also damaged , the LRC checker will not detect the error.

## Slide 27
VRC and LRC

## Slide 28
Hamming code C(7, 4) C(n,k) dmin=3

## Slide 29
The structure of the encoder and
decoder for a Hamming code

## Slide 30: Hamming Code
Parity checks are created as follow (using modulo-2)
  r0 = a2 + a1 + a0
  r1 = a3 + a2 + a1
  r2 = a1 + a0 + a3

## Slide 31: Hamming Code
The checker in the decoder creates a 3-bit syndrome (s2s1s0).
In which each bit is the parity check for 4 out of the 7 bits in the received codeword:
s0 = b2 + b1 + b0 + q0
s1 = b3 + b2 + b1 + q1
s2 = b1 + b0 + b3 + q2
The equations used by the checker are the same as those used by the generator with the parity-check bits added to the right-hand side of the equation.

## Slide 32
Logical decision made by the
correction logic analyzer
Hamming code C(7, 4) can :
detect up to 2-bit error (dmin -1)
can correct up to 1 bit error (dmin-1)/2

## Slide 33
Burst error correction using
Hamming code
Split burst error between multiple codewords

## Slide 34
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2
2. The Hamming distance d(10101, 11110) is 3 because

## Slide 35
Find the minimum Hamming distance of the coding scheme in Table
Solution
We first find all Hamming distances.
Example
The dmin in this case is 2.

## Slide 36: Practice Questions
https://pinoybix.org/2017/07/mcq-in-network-layer-internet-protocol-forouzan.html
https://edurev.in/course/quiz/attempt/-1_Test-Ipv4--IP-Packet/0decdb37-7206-4824-afdd-d47013a5c4cd