## Slide 1: IP PACKET
Header + DATA (PAYLOAD)

## Slide 3: You can think of IP packets like postal letters: the header is the envelope with all the routing information that's needed by the post office, and the payload is the letter that's read only by the recipient.

## Slide 4: STEPS HOW PACKET IS SENT?

## Slide 5: Step 1: Send packet to router

## Slide 6: Step 2: Router receives packet
When the router receives a packet, it looks at its IP header. The most important field is the destination IP address, which tells the router where the packet wants to end up.

## Slide 7: Step 3: Router forward's packet
The router has a forwarding table that helps it pick the next path based on the destination IP address. That table does not have a row for every possible IP address; there are 2322322, start superscript, 32, end superscript possible IP addresses, and that's far too much to store. Instead, the table has rows for IP address prefixes.

## Slide 8: PRACTICE QUESTIONS
https://www.khanacademy.org/computing/computers-and-internet/xcae6f4a7ff015e7d:the-internet/xcae6f4a7ff015e7d:routing-with-redundancy/e/internet-packets-and-routing-protocol

## Slide 9: KEYPOINTS
1. Connectionless
2. Datagram Service
Header (20-60 B)
+
Payload
(0-65515)
65515 (data)+20(min header)= 65535 B =2^16
Pure Data=65515

## Slide 10: FEILDS
1. Ver: 4 bits 0100 denotes Version 4 0000-1111  0000,0001,0010,0011,0100,0101,….1111
2. HLEN: 4 bits  Header length of IP Paacket
Eg. 1: If u received data of 500B it means Pure Payload= 500-20=480B
Eg.2 : How to identify the header length of a packet received is 1010. How many bytes should be there of HLEN in the received packet?
HLEN=20 to 60 B
HLEN Given = 1010  Decimal of 1010 10
But HLEN should be 20-60B; then we use multiply by 4 method. 10*4=40B  HLEN.
HLEN given value should not be from 0 to 4 as it has less than 20B. So invalid.

## Slide 11
3. Type of Service: Differentiated Services Code Point (DSCP) in IP V4 whereas Traffic Class in IP V6.
P | P | P | D | T | R | C | O
Precedence (Priority) –value 0/1
Delay – 1 for fast service otherwise 0
Throughput- rate of transfer more then 1 otherwise 0
Reliability – no packet drop, reliability high
Cost- follows shortest path (1) otherwise 0
Reserved
This reserved bit is used for DSCP (0-5 bits) + Explicit Congestion Notification (ECN) (6-7)
If the value of ECN is 11 it means it sends notification to sender that there is congestion.

## Slide 12: TIME TO LIVE
256

## Slide 13
To identify the fragmented data
Fragmented data
No Fragmented data
Tells the number of fragmented packet
No. of bytes ahead of this.